## Slide 1
10G Ethernet-to-LA1224 PCIe Datapath Driver Development
KYOCERA Weekly Report April 15, 2026

## Slide 2
Kyocera – Datapath Driver Weekly Status Report
Apr | Project Week 03
Overall Summary
Completed 10G Ethernet throughput validation: ~8.6 Gbps (single stream), ~8.7 Gbps (multi stream), zero packet loss.
Completed LDPC encode/decode validation over PCIe using dpdk-test-bbdev: DEC 17.88 Mbps, ENC 21.38 Mbps, latency 10-12 µs.
Completed PCIe raw IPC latency measurement: one-way 2.93 µs, round-trip 4.71 µs over 10,000 iterations.
All three hardware validation tests PASSED. Platform confirmed ready for DPDK driver development.
Next (WW04): SDK/DPDK familiarization, hugepage config, VFIO bind, testpmd verification, begin EAL init coding.
Tessolve Semiconductors | Kyocera SLD Laser | Confidential

## Slide 3
Kyocera – Datapath Driver Weekly Status Report
Apr | Project Week 3
WW 03
Module | Component | Description | Status | Test Status | ETA | Remarks
10G Ethernet | DPAA2 / WRIOP | iperf baseline | Completed | PASS | 13-Apr | ~8.6 Gbps single, ~8.7 Gbps multi, zero loss
dpdk-test-bbdev | BBdev / la12xx PMD | LDPC enc/dec loopback | Completed | PASS | 15-Apr | DEC 17.88 Mbps, ENC 21.38 Mbps, 10-12 µs
IPC Benchmark | BBdev RAW | PCIe throughput baseline | Completed | PASS | 15-Apr | One-way 2.93 µs, RT 4.71 µs, 10K iters
WW 04
Module | Component | Description | Status | Test Status | ETA | Remarks
- | - | - | - |  | - | No blockers.
Tessolve Semiconductors | Kyocera SLD Laser | Confidential
Module | Component | Description | Status | Test Status | ETA | Remarks
SDK/DPDK Familiarization | DPDK 22.11 / NIC | SDK study, NIC binding, DPDK APIs | Not Started |  | 21-Apr | 
Build Environment | Hugepage / VFIO | Hugepage 1 GB, VFIO bind, testpmd verify | Not Started |  | 22-Apr | 
EAL + Port Init | DPAA2 PMD | EAL init, Ethernet port config, mempool setup | Not Started |  | 22-Apr | 
Backlog
Module | Component | Description | Status | Test Status | ETA | Remarks
- | - | - | - |  | - | No blockers

## Slide 4
10G Ethernet Throughput Validation
Objective:
Validate high-speed Ethernet datapath between Host (Mac Studio) and LX2160A
Setup:
• Direct 10G connection (Mac Studio ↔ LX2160A)
• Interface configured using DPAA2 (dpmac → ethX)
• Link verified at 10 Gbps full duplex
Method:
• Used iperf3 to generate TCP traffic
• Tested both single-stream and multi-stream performance
Test | Result
Single Stream | ~8.6 Gbps
Multi Stream | ~8.7 Gbps
Packet Loss | Zero
Conclusion:
Ethernet datapath is stable and capable of high-speed data transfer.
No packet loss or retransmissions observed.
Tessolve Semiconductors | Kyocera SLD Laser | Confidential

## Slide 5
LDPC Processing Validation using LA1224 (bbdev)
Objective:
Validate LDPC hardware offload via PCIe using LA1224 FECA engine
Method:
• LX2160A sends LDPC encode/decode jobs to LA1224 over PCIe
• Communication handled via DPDK bbdev framework
• LA1224 FECA engine processes data and returns results
Metric | Result
Decode Throughput | 17.88 Mbps
Encode Throughput | 21.38 Mbps
Latency/Packet | ~10–12 µs
Test Status | ALL PASSED
Key Insight:
• Functional validation completed successfully
• Throughput can be improved with further optimization (burst size, queue depth)
Conclusion:
PCIe communication and LDPC accelerator (FECA) are working correctly.
bbdev PMD → IPC → FECA pipeline confirmed end-to-end.
Tessolve Semiconductors | Kyocera SLD Laser | Confidential

## Slide 6
PCIe Latency Measurement (Raw IPC)
Objective:
Measure raw PCIe communication latency between LX2160A and LA1224
Method:
• Sent request-response messages without any processing overhead
• Measured one-way and round-trip latency
• Executed 10,000 iterations for stability validation
Metric | Result
One-Way Latency | ~2.93 µs
Round-Trip Latency | ~4.71 µs
Iterations | 10,000
Test Status | ALL PASSED
Key Insight:
• No processing involved — pure communication delay measured
• All 10,000 test cases PASSED with stable, consistent performance
• Sub-5 µs round-trip confirms PCIe Gen3 x8 link is optimal
Conclusion:
PCIe interface is low-latency, stable, and suitable for real-time workloads.
Well within the <200 µs p99 latency target for the datapath driver.
Tessolve Semiconductors | Kyocera SLD Laser | Confidential

## Slide 7
Results at a Glance
Test | Validates | Key Numbers | Result
Test 1 | 10G Ethernet (Mac Studio ↔ LX2160A) | ~8.6 Gbps (single stream) ~8.7 Gbps (multi stream) Zero packet loss / retransmissions | PASSED
Test 2 | LDPC encode/decode over bbdev (PCIe) | DEC 17.88 Mbps, ENC 21.38 Mbps Latency 10–12 µs/packet All throughput & latency tests passed | PASSED
Test 3 | Raw PCIe DMA latency | One-way avg 2.93 µs Round-trip avg 4.71 µs 10,000 iterations — all passed | PASSED
Tessolve Semiconductors | Kyocera SLD Laser | Confidential

## Slide 8
Action Items – Weekly Status
S.No | Action Item | Status | Remarks
1 | Create folder in shared Box and update weekly status | Completed | Folder created and status updated
2 | Add buffer overflow handling technique in architecture doc | Completed | Backpressure-based flow control documented
3 | Add detailed technical points in PPT | Completed | Slides updated with detailed explanations.

## Slide 9
Performance Targets
• ≥ 8 Gbps throughput
• < 200 μs p99 latency
• < 0.001% loss
• Variable bandwidth (100-720 MHz)
10G Ethernet Network
Upstream/Downstream Traffic
RX
TX
LX2160A Host (Linux + DPDK Datapath)
WRIOP/DPAA2
QBMAN
DDR/Mempools
CPU Cores
bbdev: LDPC Enc/Dec • BG1/BG2 • z_c • Code Rate • RV • CRC • Bandwidth: 100-720 MHz
ops+DMA
writeback
PCIe Gen3 x8
~8 GB/s bandwidth
encode/decode
results
LA1224 LDPC Accelerator (FECA)
Multi-queue encode/decode • CRC check • Variable bandwidth (100-720 MHz)
Flowchart

## Slide 10
Thank You
Parthiban Balan
parthiban.pavadaibalan@tessolve.com
+91 88847 34443